## Slide 1: Optimal control of trajectory of reusable launcher in OpenMDAO/dymos
Students:
Alberto Fossà
Giuliana Elena Miceli
Tutors:
Laurent Beauregard
Joseph Morlier
Stéphanie Lizy-Destrez
June 25th 2019

## Slide 2: Outline
Context
Optimal control problem
State of the Art
2D Ascent Trajectory
2D Descent Trajectory
3D Ascent Trajectory
Conclusions & Future achievements

## Slide 3: Context
Moon and Mars Exploration
In-situ resources exploitation
Lunar Orbital Platform Gateway
credits: Lockheed Martin

## Slide 4: Context
credits: Purdue University
HALO orbits

## Slide 5: Optimal control problem: formulation
Mathematical formulation of a continuous-time optimal control problem

## Slide 6: Optimal control problem: solution
Solution of an optimal control problem - indirect methods
Calculus of variations
Euler-Lagrange first-order optimality conditions
Pontryagin Minimum Principle
Two-Points Boundary Value Problem (TPBVP)
Pros:
highly accurate solution
low computational effort
Cons:
heavy algebraic manipulation of EOMs
small region of convergence

## Slide 7: Optimal control problem: solution
Solution of an optimal control problem - direct methods
Pros:
no algebraic manipulation of EOMs
wider region of convergence
Cons:
high number of decision variables
high computational effort
Direct transcription
States and controls discretization
Non Linear Programming problem (NLP)
Iterative solution
Collocation defects driven to zero

## Slide 8: State of the Art: Tools
Direct transcription methods:
High-Order Gauss-Lobatto
Radau Pseudospectral
NLP solvers:
Gradient-based (SNOPT1, IPOPT2,3, fmincon4)
Gradient-free (PSO, DE,SA)
1Gill et al., SIAM Review, 2005
2Wächter et al., Mathematical Programming, 2006
3HSL, http://www.hsl.rl.ac.uk/
4Matworks, https://www.mathworks.com/
5Patterson et al., ACM Trans. Math. Softw., 2014
6Gray et al., Structural and Multidisciplinary Optimization, 20197
7Hendricks et al., AIAA, 2017
Libraries:
GPOPS-II5 (MATLAB4)
OpenMDAO/dymos6,7 (Python)

## Slide 9: Implementation
Optimal control problem for spacecraft trajectory optimization
Direct transcription
High-Order Gauss-Lobatto, OpenMDAO/dymos library
NLP problem
IPOPT solver, linear solver MA57
Validation
IVP from initial conditions and optimal control profile, simulate method

## Slide 10: 2D Ascent Trajectory: EOMs
Equations of motions (EOMs):
θ
T
V
v
u
r

## Slide 11: 2D Ascent: Optimal control problem

## Slide 12: 2D Ascent: Solutions
Ascent Trajectory | Time of Flight | Propellant consumption
Constant Thrust | 476.13 s | 36.80%
Variable Thrust | 3697.56 s | 33.64%
Semianalytic initial guess | 3803.26 s | 32.81%
Variable Thrust, Minimum safe altitude | 3367.77 s | 35.50%
Target orbit altitude | 86.87 km
Isp | 450 s
Initial thrust/weight ratio | 2.1
Common parameters:
Proposed solutions:

## Slide 13: 2D Ascent: Constant thrust
Time of Flight | Propellant consumption
476.13 s | 36.80%

## Slide 14: 2D Ascent: Variable thrust
Time of Flight | Propellant consumption
3697.56 s | 33.64%

## Slide 15: 2D Ascent: Minimum safe altitude
Path constraint to avoid lunar highlands:
Seminanalytic initial guess:
Three-phases trajectory:
powered phase at constant radius r=R
Hohmann transfer
impulsive injection burn

## Slide 16: 2D Ascent: Minimum safe altitude
Ascent Trajectory | Time of Flight | Propellant consumption
Initial guess | 3803.26 s | 32.81%
Variable Thrust, Minimum safe altitude | 3367.77 s | 35.50%

## Slide 17: 2D Ascent: Minimum safe altitude
h | 5.0 km
s | 100

## Slide 18: 2D Descent: Optimal control problem

## Slide 19: 2D Descent Trajectory
Descent Trajectory without final constraints
Descent Trajectory with final constraints
 | Time of Flight | Propellant consumption
Free | 999.05 s | 48.51%
Vertical constrained | 1034.77 s | 50.24%
Parking orbit altitude | 100 km
Powered descent phase initial altitude | 15 km
Vertical phase initial altitude | 4 km
Isp | 310 s
initial thrust/weight ratio | 0.90

## Slide 20: 3D Ascent: EOMs
Equations of motion (EOMs):

## Slide 21: 3D Ascent: Optimal control problem

## Slide 22: 3D Ascent: Constant thrust
Polar orbit - coplanar transfer
Type of orbit | Eccentricity | Inclination | Argument of perilune | Semimajor axis | Time of flight | Propellant consumption
Polar | 0 | 90° | - | 1824.27 km | 476.29 s | 36.81%
Higly elliptical | 0.7 | 60° | 270° | 6080.90 km | 876.73 s | 67.76%
Highly elliptical orbit - out-of-plane manoeuvre

## Slide 23: Conclusions & Future achievements
Main issues:
Understanding OpenMDAO/dymos framework
Inadequate NLP solvers (SLSQP)
Poor State of the Art
Difficulties while selecting correct transctiption
High sensitivity to variables scaling
3D ascent trajectory improvements:
Variable thrust
Limits on attitude rates
Constraints on ground clearance
Other developments:
3D descent trajectory
High fidelity gravity model
Moon rotation

## Slide 24: Selected bibliography
Benson, David. A Gauss Pseudospectral Transcription for Optimal Control. Massachusetts Institute of Technology, 2005, https://dspace.mit.edu/handle/1721.1/28919.
Find Minimum of Constrained Nonlinear Multivariable Function. https://www.mathworks.com/help/optim/ug/fmincon.html?s_tid=srchtitle.
Gill, Philip E., et al. ‘SNOPT: An SQP Algorithm for Large-Scale Constrained Optimization’. SIAM Review, vol. 47, no. 1, Jan. 2005, pp. 99–131. doi:10.1137/S0036144504446096.
Gray, Justin S., et al. ‘OpenMDAO: An Open-Source Framework for Multidisciplinary Design, Analysis, and Optimization’. Structural and Multidisciplinary Optimization, vol. 59, no. 4, Apr. 2019, pp. 1075–104. doi:10.1007/s00158-019-02211-z.
Hendricks, Eric S., et al. ‘Simultaneous Propulsion System and Trajectory Optimization’. 18th AIAA/ISSMO Multidisciplinary Analysis and Optimization Conference, American Institute of Aeronautics and Astronautics, 2017. doi:10.2514/6.2017-4435.
HSL, A Collection of Fortran Codes for Large Scale Scientific Computation. http://www.hsl.rl.ac.uk/.
Longuski, Jim, et al. Optimal Control with Aerospace Applications. Springer ; Published jointly by Microcosm Press, 2014.
Ma, Lin, et al. ‘Trajectory Optimization for Lunar Rover Performing Vertical Takeoff Vertical Landing Maneuvers in the Presence of Terrain’. Acta Astronautica, vol. 146, May 2018, pp. 289–99. doi:10.1016/j.actaastro.2018.03.013.
Patterson, Michael A., and Anil V. Rao. ‘GPOPS-II: A MATLAB Software for Solving Multiple-Phase Optimal Control Problems Using Hp-Adaptive Gaussian Quadrature Collocation Methods and Sparse Nonlinear Programming’. ACM Transactions on Mathematical Software, vol. 41, no. 1, Oct. 2014, pp. 1–37. doi:10.1145/2558904.
Ramanan, R. V., and Madan Lal. ‘Analysis of Optimal Strategies for Soft Landing on the Moon from Lunar Parking Orbits’. Journal of Earth System Science, vol. 114, no. 6, Dec. 2005, pp. 807–13. doi:10.1007/BF02715967.
Shirazi, Abolfazl, et al. ‘Spacecraft Trajectory Optimization: A Review of Models, Objectives, Approaches and Solutions’. Progress in Aerospace Sciences, vol. 102, Oct. 2018, pp. 76–98. doi:10.1016/j.paerosci.2018.07.007.
Topputo, F., and C. Zhang. ‘Survey of Direct Transcription for Low-Thrust Space Trajectory Optimization with Applications’. Abstract and Applied Analysis, vol. 2014, 2014, pp. 1–15. doi:10.1155/2014/851720.
Wächter, Andreas, and Lorenz T. Biegler. ‘On the Implementation of an Interior-Point Filter Line-Search Algorithm for Large-Scale Nonlinear Programming’. Mathematical Programming, vol. 106, no. 1, Mar. 2006, pp. 25–57. doi:10.1007/s10107-004-0559-y.

## Slide 25
Thank you for your attention
Any question?